## Slide 1
TEAM VOLTERE | ELEC-03
Design and Implementation of an
8-bit Pipelined Microprocessor in Verilog
A 5-stage, hazard-resilient CPU with recursive subroutines,
precise exception handling, and memory-mapped peripherals
Indian Institute of Technology Indore
Science & Technology Council
IITISoC 2026

## Slide 2
TEAM VOLTERE | IITISoC 2026
The challenge: execute a custom ISA safely in a pipeline
• Immediate-value loading and register arithmetic
• Data-memory load and store operations
• Conditional and unconditional control flow
• Correct execution despite data and control hazards
• Fully synthesizable Verilog implementation
Our objective was to keep hazard handling inside hardware, so assembly programs do not need inserted NOP instructions.
Team VOLTERE | 8-bit Pipelined Microprocessor
02

## Slide 3
TEAM VOLTERE | IITISoC 2026
We built a complete 8-bit embedded processor system
8-bit data path | 16-bit instruction word | 8 general-purpose registers
28 implemented instructions
IF
Fetch
→
ID
Decode
→
EX
Execute
→
MEM
Memory
→
WB
Write-back
Hardware forwarding | Load-use stall logic | Branch prediction
Subroutine calls | Exceptions | UART | ADC | GPIO | PWM
Team VOLTERE | 8-bit Pipelined Microprocessor
03
IF: PC, Instruction Memory, Branch Predictor
ID: Control Unit, Register File, Immediate Extension
EX: ALU, MAC, Forwarding Unit, Branch Resolution, CP0
MEM: Data Memory, UART, ADC, GPIO, PWM
WB: ALU result, memory data, immediate, or JAL return address

## Slide 4
TEAM VOLTERE | IITISoC 2026
The Entire Architecture at a glance
Team VOLTERE | 8-bit Pipelined Microprocessor
04

## Slide 5
TEAM VOLTERE | IITISoC 2026
A compact register file and 256-byte address space simplify the CPU
REGISTER FILE
• R0-R7, each 8 bits wide
• R0 is hardwired to zero
• Three read ports support MAC
DATA MEMORY
0x00 - 0xF9
General-purpose RAM
0xFA 0xFB 0xFC 0xFD 0xFE 0xFF
Team VOLTERE | 8-bit Pipelined Microprocessor
06
Three read ports allow the MAC instruction to read its accumulator and two input operands in one cycle, avoiding an extra pipeline stage or cycle.
UART Status UART Receiver Data Register UART Transmitter Data Register External ADC Inputs External Digital Inputs PWM Motor Duty Cycle

## Slide 6
TEAM VOLTERE | IITISoC 2026
A fixed 16-bit encoding supports 28 instructions with simple decode
R-Type
Opcode | Rd | Rs1 | Rs2 | Unused
I-Type
Opcode | Rd | Immediate[7:0]
ADDI-Type
Opcode | Rd | Rs1 | Immediate[4:0]
Branch
Opcode | Rs1 / Rd | Target / Offset[7:0]
System
Opcode | Rs1 | Unused
Opcode field: instruction[15:11]
Team VOLTERE | 8-bit Pipelined Microprocessor
07

## Slide 7
TEAM VOLTERE | IITISoC 2026
The ISA covers arithmetic, control flow, DSP, system control, and I/O access
Arithmetic and logic
ADD SUB AND OR XOR
SHL SHR SLT ROL ROR
Data movement
LDI LDD STR STD
ADDI
Control flow
JMP JZ JNZ JGT
JAL JR HALT
DSP and system
MUL MAC
RETI TRAP ERET MFC0
Team VOLTERE | 8-bit Pipelined Microprocessor
08

## Slide 8
TEAM VOLTERE | IITISoC 2026
Forwarding resolves immediate register dependencies without NOPs
Without forwarding (2 NOPs wasted):
Cycle : 1 2 3 4 5 6 7 8
ADD r3 : IF ID EX MEM WB
NOP : IF ID EX MEM WB
NOP : IF ID EX MEM WB
SUB r4 : IF ID EX MEM WB ← reads r3 from regfile in WB
With forwarding (0 NOPs, 0 stalls):
Cycle : 1 2 3 4 5
ADD r3 : IF ID EX MEM WB SUB r4 : IF ID EX ← r3 forwarded from EX/MEM
Forwarding is available for RS1, RS2, and RS3..
Team VOLTERE | 8-bit Pipelined Microprocessor
09
ADD r3, r1, r2
SUB r4, r3, r5 ← receives r3 through forwarding

## Slide 9
TEAM VOLTERE | IITISoC 2026
The only unavoidable RAW dependency receives one controlled bubble
LDD r5, [r1 + 0]
ADD r4, r5, r2
The loaded value is available only after the MEM stage.
1. Freeze PC
2. Freeze IF/ID
3. Insert bubble into ID/EX
4. Forward loaded value after MEM
One bubble preserves correctness without stalling unrelated instructions.
Team VOLTERE | 8-bit Pipelined Microprocessor
10
Cycle : 1 2 3 4 5 6 7 8
LDD r5 : IF ID EX MEM WB
↑
data appears HERE (start of WB)
ADD r4 : IF ID EX ← needs r5 HERE
The Solution
The Problem

## Slide 10
TEAM VOLTERE | IITISoC 2026
A 32-entry BTB and BHT reduce control-hazard cost
Branch Target Buffer
32 entries, indexed by PC[4:0]
Each entry stores:
• Valid bit
• Tag (full PC address)
• Predicted Target Address
Hit condition:
valid_btb[PC[4:0]] == 1
AND tag == current PC
Branch History Table
32 entries, 1-bit per entry
1 = predict TAKEN → fetch from BTB target
0 = predict NOT TAKEN → fetch PC + 1
Updated every time branch resolves in EX
JR/RETI/ERET always flush: Their target addresses live in registers (rs1, EPC) which are only known in the EX stage — the BTB cannot cache a value it has never seen at fetch time.
Team VOLTERE | 8-bit Pipelined Microprocessor
11

## Slide 11
TEAM VOLTERE | IITISoC 2026
Both IITISoC bonus tasks were implemented and verified
BONUS 1
Recursive subroutine calls
JAL + JR + software stack
Verified with recursive factorial
BONUS 2
Precise exception handling
EPC + CAUSE + vector + ERET
Overflow, illegal instruction, TRAP
These are fully synthesizable RTL features, not software-only demonstrations.
Team VOLTERE | 8-bit Pipelined Microprocessor
12

## Slide 12
TEAM VOLTERE | IITISoC 2026
JAL and JR implement genuine function calls and returns
JAL r7, offset
R7 = PC + 1
PC = PC + SignExt(offset)
JR r7
PC = R7
CALLER
JAL
CALLEE
→
→
JR returns to caller continuation
The JAL link value is forwarded, so return control flow does not require manually inserted NOPs.
Team VOLTERE | 8-bit Pipelined Microprocessor
13

## Slide 13
TEAM VOLTERE | IITISoC 2026
Recursive factorial proves that nested stack frames are preserved
LDI r6, 0x70
LDI r1, 5
JAL r7, fact
STD r1, [0xA0]
HALT
fact: JZ r1, fact_base
STR r7, [r6 + 0]
STR r1, [r6 + 1]
ADDI r6, r6, -2
fact(5)
fact(4)
fact(3)
…
Each frame saves R7 (return address) and R1 (n).
Final result: memory[0xA0] = 0x78 = 120
Team VOLTERE | 8-bit Pipelined Microprocessor
14

## Slide 14
TEAM VOLTERE | IITISoC 2026
Simulation confirms recursive control flow and the correct factorial result
Use the saved waveform: sim/bonus1/bonus1_factorial.vcd
WAVEFORM EVIDENCE
• PC changes during JAL and JR
• R6 moves as stack frames are allocated and released
• R7 stores and restores return addresses
• Result is written to memory[0xA0]
• Final result = 120
PASS Bonus 1: recursive factorial result = 120
Team VOLTERE | 8-bit Pipelined Microprocessor
15

## Slide 15
TEAM VOLTERE | IITISoC 2026
The exception unit captures fault state and redirects execution safely
EPC
Exact PC of faulting instruction
CAUSE
1: overflow | 2: illegal | 3: TRAP
VECTOR
PC redirects to 0x80
MFC0 / ERET
Read state / resume at EPC + 1
Fault → Capture EPC/CAUSE → Flush unsafe instructions → PC = 0x80 → Handler → ERET or HALT
Team VOLTERE | 8-bit Pipelined Microprocessor
16

## Slide 16
TEAM VOLTERE | IITISoC 2026
Overflow is contained, corrected by the handler, and normal execution resumes
LDI r1, 200
LDI r2, 100
ADD r3, r1, r2 ← overflow at PC = 2
STD r3, [0xAA]
SUB r4, r1, r2
STD r4, [0xAB]
CAUSE = 1
R3 = 0xFF
ERET
Verified: memory[0xAA] = 0xFF
Verified: memory[0xAB] = 100
Waveform asset: sim/bonus2/bonus2_exceptions.vcd
Team VOLTERE | 8-bit Pipelined Microprocessor
17

## Slide 17
TEAM VOLTERE | IITISoC 2026
An unsupported opcode is detected before it can corrupt memory
LDI r1, 10
LDI r2, 20
.word 0xD800 ← unsupported opcode 11011
ADD r3, r1, r2 ← must never execute
STD r3, [0xBB]
Fault address: PC = 2
CAUSE = 2
Handler writes memory[0xFF] = 0xEE
Handler enters HALT
Verified: memory[0xBB] remains 0x00
Team VOLTERE | 8-bit Pipelined Microprocessor
18

## Slide 18
TEAM VOLTERE | IITISoC 2026
TRAP records the exact faulting PC and prevents unsafe code from running
LDD r1, [r0 + 0x10]
TRAP ← deliberate fault at PC = 1
LDI r2, 0x99
STD r2, [0xCC] ← must never execute
CAUSE = 3
MFC0 r5, EPC
STD r5, [0xDD]
HALT
Verified: EPC = 1 | memory[0xDD] = 1
Verified: memory[0xCC] remains 0x00
Team VOLTERE | 8-bit Pipelined Microprocessor
19

## Slide 19
TEAM VOLTERE | IITISoC 2026
Ordinary load/store instructions provide the complete peripheral interface
0xFA
UART status: overrun, TX-ready, RX-valid
0xFB
UART received data
0xFC
UART transmit data
0xFD
External ADC input
0xFE
External digital input
0xFF
PWM motor duty-cycle register
UART operates at 115200 baud. PWM provides 256 duty-cycle levels.
Team VOLTERE | 8-bit Pipelined Microprocessor
20

## Slide 20
TEAM VOLTERE | IITISoC 2026
The saved verification suite covers CPU function, hazards, peripherals, and UART communication
• Arithmetic, logic, memory, and control instructions
• EX→EX and MEM→EX forwarding; load-use stalling; R0 protection
• Branch prediction, JAL/JR, and pipeline flush recovery
• Exceptions, MFC0, ERET, and interrupt support
• GPIO, ADC, PWM, UART TX, and UART TX→RX loopback
UART loopback: transmitted 0x35, polled RX-valid, received 0x35, and loaded 0x35 into R2.
Team VOLTERE | 8-bit Pipelined Microprocessor
21

## Slide 21
TEAM VOLTERE | IITISoC 2026
Integrated simulation proves pipeline, MAC, memory, PWM, and evaluation-program correctness
MASTER SUITE
• R3 = 30
• MAC result R4 = 244
• memory[0x60] = 244
• Loaded R5 = 244
• SUB result R6 = 214
• PWM duty cycle = 214
END-EVALUATION PROGRAM
• R1 = 50
• R3 = 25
• R5 = 48
• R6 = 21
• Saved R7 = 33
• Shifted result = 132
All saved simulations were rerun successfully for this presentation.
Team VOLTERE | 8-bit Pipelined Microprocessor
22

## Slide 22
TEAM VOLTERE | IITISoC 2026
The implemented Kintex-7 design is lightweight and achieves 135.8 MHz
Slice LUTs
808 / 41,000
1.97%
Registers
361 / 82,000
0.44%
Distributed RAM
84 LUTs
-
DSP48 slices
0 / 240
0%
Bonded I/O
22 / 300
7.33%
Fmax = 135.8 MHz
Target device: xc7k70tfbv676-1
Team VOLTERE | 8-bit Pipelined Microprocessor
23

## Slide 23
TEAM VOLTERE | IITISoC 2026
Post-implementation timing and power results demonstrate practical hardware viability
TIMING
50 MHz target
WNS = +11.598 ns
200 MHz stress target
WNS = -2.363 ns
Critical path = 7.363 ns
5-stage latency = 36.815 ns
POWER
Total on-chip power: 100 mW
Dynamic power: 19 mW
Static power: 81 mW
Junction temperature: 25.2 °C
Physical implementation data from Vivado 2025.2
Team VOLTERE | 8-bit Pipelined Microprocessor
24

## Slide 24
TEAM VOLTERE | IITISoC 2026
Separating memory access from execution improved timing
Earlier 4-stage path
ALU → address generation
→ memory access
Too much combinational work
in one clock period
Final 5-stage path
IF → ID → EX → MEM → WB
Memory access is isolated
from ALU execution
The extra stage improves clock-frequency potential; the load-use detector absorbs the additional dependency latency.
Team VOLTERE | 8-bit Pipelined Microprocessor
05

## Slide 25
TEAM VOLTERE | IITISoC 2026
A compact CPU that goes beyond the baseline challenge
• Synthesizable 5-stage, 8-bit pipelined microprocessor
• 28-instruction custom ISA
• Forwarding, load-use stalls, and branch prediction
• Recursive JAL/JR support with a software stack
• EPC, CAUSE, exception vectoring, MFC0, and ERET
• UART, ADC, GPIO, and PWM memory-mapped peripherals
• Verified simulations and 135.8 MHz post-implementation Fmax
Thank you
Team VOLTERE | 8-bit Pipelined Microprocessor
25